## Slide 1: Tutorial 2
Paper
Pen
Calculator

## Slide 2
sampling period T = 1/Fs
sampled signal x(n) = x(nT) = x(t=nT)
x(t) with frequency Fx  aliased signal xa(t) with frequency Fa  Fx
  Definition 1 (based on sampling): Fa = Fx + k.Fs  many sols
  Definition 2 (based on rescontruction): Fa = (Fx + k.Fs) [-Fs/2  Fs/2]  only 1 sol

## Slide 3
x(t) with frequency Fx  aliased signal xa(t) with frequency Fa = (Fx + k.Fs)  [-Fs/2  Fs/2]
F1 = 2, F2 = 6, F3 = 10 (Hz)
F1aliased = 2, F2aliased = -2, F3aliased = 2
 xaliased(t) = 10sin(2..2.t) + 10sin(2..(-2).t) + 5sin(2..2.t)
xaliased(t) x(t) ?
xaliased(n) = x(n) ?
x(n) = 10sin(4..n.T) + 10sin(12..n.T) + 5sin(20..n.T)
xaliased(n) = 10sin(2..2.n.T) + 10sin(2..(-2).n.T) + 5sin(2..2.n.T)
T = 1/8
10sin(12..n.T) = 10sin(12..n/8)= 10sin(12..n/8-2..n)= 10sin(-4..n/8)
10sin(2..(-2).n.T) = 10sin(-4..n/8)

## Slide 4: Q1 (answer_def2)
Fs = 8Hz
xa_only1(t) = 10sin(2..2.t) + 10sin(2..(-2).t) + 5sin(2..2.t)
Fs = 14Hz
xa_only1(t) = 10sin(2..2.t) + 10sin(2..6.t) + 5sin(2..3.t)

## Slide 5
x(t) with frequency Fx  aliased signal xa(t) with frequency Fa = Fx + k.Fs (k  0)
F1 = 2, F2 = 6, F3 = 10 (Hz)
F1aliased = 10 (or -6, 18, …), …
 xaliased(t) = 10sin(2..10.t) + 10sin(12..t) + 5sin(20..t)
xaliased(t) x(t) ?
xaliased(n) = x(n) ?
x(n) = 10sin(4..n.T) + 10sin(12..n.T) + 5sin(20..n.T)
xaliased(n) = 10sin(2..10.n.T) + 10sin(12..n.T) + 5sin(20..n.T)
T = 1/8
10sin(4..n.T) = 10sin(4..n/8)= 10sin(.n/2)
10sin(2..10.n.T) = 10sin(2..10.n/8)=10sin(2..10.n/8 – 2..n)=10sin(.n/2)

## Slide 6: Q1 (answer_def1)
Fs = 8Hz
xa1(t) = 10sin(20t) + 10sin(12t) + 5sin(20t)
xa2(t) = 10sin(36t) + 10sin(12t) + 5sin(20t)
Fs = 14Hz
xa1(t) = 10sin(32t) + 10sin(12t) + 5sin(20t)
xa2(t) = 10sin(60t) + 10sin(12t) + 5sin(20t)

## Slide 7
Nyquist reconstructed frequency range: [-Fs/2  Fs/2]
Sampling signal x(t) with frequency F  reconstructed signal xa(t) with frequency Fa = (F + k.Fs) [-Fs/2  Fs/2]

## Slide 8: Q2 (answer)
x(t) = sin(6t) + 2sin(6t).cos(4t) = sin(6t) + sin(10t) + sin(2t)
Fs = 4
Nyquist reconstructed frequency range: [-2  2]
fa1 = (3 + k14)  [-2  2] = -1
fa2 = (5 + k24)  [-2  2] = 1
fa3 = (1 + k34)  [-2  2] = 1
Reconstructed signal xa(t) = sin(-2t) + sin(2t) + sin(2t) = sin(2t)

## Slide 9
Sampling period T = 1/Fs
x(n) = xa(t = nT)

## Slide 10: Q3 (answer)

## Slide 11
Sampling period T
x(n) = xa(t = n.T)

## Slide 12: Q4 (answer)

## Slide 13: Q4 (answer)

## Slide 14
CT Fourier Transform of xa(t) = cos(w0.t) = cos(2.pi.f0.t):
Xa(w) = pi.(w + w0) + pi.(w - w0) {or Xa(f) = 0.5(f + f0) + 0.5(f - f0) }
Sampling period T
DT Fourier Transform of xd(n) = xa(t=nT) = cos(wn.n)
Xd(w) = pi.(w + wn) + pi.(w - wn) but wn [-pi pi]

## Slide 15: Q5 (answer a)

## Slide 16: Q5 (answer)

## Slide 17: Q5 (answer b)
T = 2ms
x(n) = cos(800.pi.n.2/1000) = cos(1,6.pi.n) = cos(1,6.pi.n – 2.pi.n) = cos(-0,4.pi.n) = cos(0,4.pi.n)
Xd(w) = pi.(w – 0,4.pi) + pi.(w + 0,4.pi)
= pi.(w + 0,4.pi) + pi.(w - 0,4.pi)

## Slide 18: Q5 (answer c)
Tmax = ? (no aliasing)
wn = pi  w0.Tmax = pi  Tmax = pi/w0 = pi/(800.pi) = 1/800

## Slide 20
HdB = 20.log10(H)  H = 10^(HdB/20)
H = 1  HdB = 0 dB
1 octave = 2 times, 2 octaves = 4 times, 3 octaves = 8 times, …
1 decade = 10 times, 2 decades = 100 times, 3 decades = 1000 times, …

## Slide 21: Q6 (answer)

## Slide 22: Q6 (answer)

## Slide 23: Q6 (answer)